| Antenna | Date | Operator(s) |
| --- | --- | --- |
| ea04 | 2/21/2008 | David Midgett |

Open a shell window on EVA, login as evlaops to run most of these procedures. The commands requested at the shell prompt are in the path for user evlaops.

| Task | Date | Op. initials | Pass or Fail |
| --- | --- | --- | --- |
| Mib Connectivity | 2/21/2008 | DM | PASS |

Procedure:

At the shell prompt, type:

% getAntennaMibList

Enter the antenna number when prompted.  It may take 1-2 minutes for the Mib list to come up.   If it does this successfully, it will look something like this:

MIB       status 
  ------    ------ 
  ACU       normal 
  D301      normal 
  D302      normal 
  D303      normal 
  D304      normal 
  L301-1    normal 
  L301-2    normal 
  L302-1    normal 
  L302-2    normal 
  L304      normal 
  L305      normal 
  L352      normal 
  T304-A    normal 
  T304-B    normal 
  T304-C    normal 
  T304-D    normal 

  followed by the message: 
  The MIB connectivity test PASSED! 

  If it says FAILED instead of PASSED, then they should note which of the 
  MIBs failed in the list, and write up a maintenance form.

| Task | Date | Op. initials | Pass or Fail |
| --- | --- | --- | --- |
| Database Quantities | 2/21/2008 | DM | PASS |

At the shell prompt, type:
  % getAntennaDbEntries 
    Enter the antenna number when prompted.  This one will go much more 
  quickly than #1 above, and will print out something like (if successful): 
  database quantity     status 
  --------------------     ------ 
  DCS                        normal 
  LOCATION           normal 
  1.5GHz                   normal 
  6GHz                      normal 
  10GHz                    normal 
  22GHz                    normal 
  45GHz                    normal 

  followed by the message: 
  The database quantities test PASSED! 

  If it says FAILED instead of PASSED, then note which of the 
  quantities failed in the list and report the failures in a maintenance form.

| Task | Date | Op. initials | Pass or Fail |
| --- | --- | --- | --- |
| E-Stops | 2/21/2008 | DM | PASS |

Verify E-stops are off via Wye-Mon.  This will work for 13,14,16,18 only.  Call out to have someone release E-stops if this fails.  Note: We cannot check out 24 and subsequent EVLA antennas unless M302/303 is installed.

| Task | Date | Op. initials | Pass or Fail |
| --- | --- | --- | --- |
| ACU | 2/21/2008 | DM | PASS |

Verify ACU is functioning by doing the following through the ACU screen:

- place in DPM

- send elevation to 80 degrees

- park antenna at 88 degrees

If any of this fails, the check fails; report in a maintenance form.

| Task | Date | Op. initials | Pass or Fail |
| --- | --- | --- | --- |
| L305 in sync | 2/21/2008 | DM | PASS |

Open the Operators’ Array Screen and queue the script:

/home/mchost/evla/scripts/operations/Xsysstart.py

Watch the alert messages to make sure the L305 sync detection alert is not triggered within 2 minutes.  If an alert occurs, the check fails; report in a maintenance form.

| Task | Date | Op. initials | Pass or Fail |
| --- | --- | --- | --- |
| Noise tube switching | 2/21/2008 | DM | PASS |

Continue running script from above (/home/mchost/evla/scripts/operations/Xsysstart.py)

Check the T5 reading from the BB overlay.  To pass, the values needs to be >1.0 and stable to 1-2%.  Report failure in a maintenance form.

| Task | Date | Op. initials | Pass or Fail |
| --- | --- | --- | --- |
| Synthesizers locked | 2/21/2008 | DM | PASS |

Continue running script from above (/home/mchost/evla/scripts/operations/Xsysstart.py)

Watch for any L30? Alerts.  Report failures in a maintenance form.

| Task | Date | Op. initials | Pass or Fail |
| --- | --- | --- | --- |
| Fringes – C Band | 2/21/2008 | DM | PASS |
| X Band | 2/21/2008 | DM | PASS |

Verify that the antenna fringes.  Must include some VLA antennas.

- Use xsysstart evla script for evla and sysstart on the VLA  to check X-band. Check D10/F display to verify fringes are present and stable.

- Use csysstart evla script for evla and sysstart on the VLA  to check C-band.  Check D10/F display to verify fringes are present and stable.

If weak or no fringes detected, report failure in a maintenance form.

| Task | Date | Op. initials | Pass or Fail |
| --- | --- | --- | --- |
| Delays | 2/21/2008 | DM | PASS |

Check via the Modcomp DELAY program. Follow the procedure used for VLA antennas.

| Task | Date | Op. initials | Pass or Fail |
| --- | --- | --- | --- |
| Pointing | 2/21/2008 | DM | PASS |

Currently, this is done by Ken Sowinski.  Check with Ken to verify pointing has been done.  Note bands with good pointing.

| Task | Date | Op. initials | Pass or Fail |
| --- | --- | --- | --- |
| Baselines | 2/21/2008 | DM | PASS |

Currently, this is done by Ken Sowinski.  Check with Ken to verify baselines have been  updated.